## Slide 1: ROAD INFRASTRUCTURE SAFETY MANAGEMENT DIRECTIVE (RISM)
Harry Cullen
SPM Road Safety, National Roads Authority, Ireland
Chairman of CEDR Technical Group Road Safety
 hcullen@nra.ie
www.nra.ie
Link to Directive -- http://eur-lex.europa.eu/LexUriServ/LexUriServ.do?uri=CELEX:32008L0096:EN:HTML
Notes: Road Infrastructure Safety Management Directive
31/07/26
EU Road Infrastructure Safety Directive - Kilkenny October 2010
<number>

## Slide 2: The Directive
EU Road Infrastructure Safety Management Directive – April 2012
Directive requires the establishment and implementation of procedures relating to:
  Road Safety Impact Assessments
  Road Safety Audit & Training Requirements
  Safety Ranking & Management of the road network in operation
  Road Safety Inspection
  Also includes:
    Best Practice Exchange
    Data Management requirements
    Adoption of Guiodelines.
Directive adopted on the 19th November 2008
Came into force 19th December 2010

## Slide 3: The Directive
This Directive will apply to roads which are part of the trans-European road network (TERN) whether they are at design stage, under construction or in operation.
EU Road Infrastructure Safety Management Directive – April 2012

## Slide 4: The Directive
NRA HD 14/12
Road Safety Management Procedures for National Roads in Ireland
EU Road Infrastructure Safety Management Directive – April 2012

## Slide 5: The Directive
This Directive will apply to roads
which are part of the trans-European road network (TERN) whether they are at
design stage, under construction or in operation.
if Member States just apply the Directive on the TERN, are they creating a double standard?
EU Road Infrastructure Safety Management Directive – April 2012

## Slide 6: The Directive
EU Road Infrastructure Safety Management Directive – April 2012
Directive preamble (6)
Will Member States use Preamble 6 as an excuse to “Do Nothing”?

## Slide 7: Art 3, Road safety impact assessment for infrastructure project
EU Road Infrastructure Safety Management Directive – April 2012

## Slide 8: Art 3, Road safety impact assessment for infrastructure project
EU Road Infrastructure Safety Management Directive – April 2012
Definition – Road Safety Impact Assessment
1)."road safety impact assessment" means a strategic comparative analysis of the impact of a new road or a substantial modification to the existing network on the safety performance of the road network.
Substantial Modification

## Slide 9: Art 3, Road safety impact assessment for infrastructure project
EU Road Infrastructure Safety Management Directive – April 2012
  RSIA will now be a stand alone document, prepared by the designer. It is an integral part of the design process and is to be produced by the design team.
  The road safety impact assessment shall indicate the road safety considerations which contribute to the choice of the proposed solution. It shall further provide all relevant information necessary for a cost-benefit analysis of the different options assessed.

## Slide 10: Art 4, Road Safety Audits for Infrastructure Projects
EU Road Infrastructure Safety Management Directive – April 2012

## Slide 11: Certificate of Competence
EU Road Infrastructure Safety Management Directive – April 2012
Road Safety Audit - Certificate of Competence
  Any consistency across the EU?
  Will there be legal challenges?
Art 4, Road Safety Audits for Infrastructure Projects
Irish DMRB standards state:
1.11 Audit Team:
  A competent Audit team consists of a minimum of two persons, independent of the Designer and approved by the Overseeing Organisation. Current & future NRA training and experience requirements for Audit Teams are available on the NRA website. www.nra.ie/Publications/RoadSafety

## Slide 12: Art 4, Road Safety Audits for Infrastructure Projects
Issues with the Early Operation road safety audit
  Definition of “Early”
  in Ireland our collision data is usually 18 months to 2 years late - so we will have no collision data for this audit.
  Why not use RSI?
  What is the difference between RSI and early operation road safety audit?
  Why not use collision cluster analysis when the data becomes available?
EU Road Infrastructure Safety Management Directive – April 2012

## Slide 13: Art 5, Safety ranking and management of the road network
EU Road Infrastructure Safety Management Directive – April 2012

## Slide 14: Art 5, Safety ranking and management of the road network
EU Road Infrastructure Safety Management Directive – April 2012
Definition – Safety Ranking and Management of the road network
5)."ranking of high accident concentration sections" means a method to identify, analyse and rank sections of the road network which have been in operation for more than three years and upon which a large number of fatal accidents in relation to traffic flow have occurred
Implications for Ireland
The management of accident remedial measures and high-risk road sections has been an integral part of the work of the Authority for many years now. Our work in the identification of collision clusters throughout the network using different GIS procedures is recognised as best practice
A new procedures standard has been written to document our existing work practices in this area.

## Slide 15: Art 6, Road Safety Inspections
EU Road Infrastructure Safety Management Directive – April 2012

## Slide 16: Art 6, Road Safety Inspections
EU Road Infrastructure Safety Management Directive – April 2012
Definition – Road Safety Inspections
7)."safety inspection" means an ordinary periodical verification of the characteristics and defects that require maintenance work for reasons of safety;

## Slide 17: Art 6, Road Safety Inspections
EU Road Infrastructure Safety Management Directive – April 2012
In Ireland, like most of Europe, the TERN network consists of our motorway network plus some single carriageway roads.
  By focusing RSI on the TERN network will this Directive take funding away from other non-TERN single carriageway roads?
  Ireland have tried to avoid this by agreeing to carry out RSI on all national roads

## Slide 18: Art 6, Road Safety Inspections
EU Road Infrastructure Safety Management Directive – April 2012
Who carries out road safety inspections?
  Who does the recommendations based on the report?
  what role (if any) have the local authorities this process ?
    they cannot inspect their own roads!

## Slide 19: Art 6, Road Safety Inspections
EU Road Infrastructure Safety Management Directive – April 2012
How do you stop “Over The Top” report recommendations from RSI – from either a local authority or a consultant wanting a “Rolls-Royce” solution to every problem?
  Ireland have split the report and the recommendations –
    NRA road safety engineers will make the recommendations based on report provided by consultants or regional road offices.

## Slide 20: Art 6, Road Safety Inspections
EU Road Infrastructure Safety Management Directive – April 2012
Article 6 – Health and Safety at Road Works
This Directive means that Road Safety and Health & Safety at road works are coming closer together

## Slide 21: Art 6, Road Safety Inspections
EU Road Infrastructure Safety Management Directive – April 2012
Article 6 – Health and Safety at Road Works
  notification of road works schemes
  inspection regime
  statutory undertakers – what contact lists exist
  who inspects what?
    Inspections of roadwork sites
    Inspections of the procedures on roadwork sites to ensure that standards and guidelines are being applied

## Slide 22: Art 6, Road Safety Inspections
EU Road Infrastructure Safety Management Directive - – April 2012
Procedures for road works sites also mention in this Article.
Art 6.4 of the Directive also says:
  They shall also implement an appropriate inspection scheme to ensure that those guidelines are properly applied.
This means that an inspection scheme needs to be established:
  by NRA to ensure that those guidelines are properly applied on TERN network road works sites (in Ireland, on all national roads), and
  by Local Authorities to ensure that those guidelines are properly applied on:
    LA TERN network road works sites (in Ireland, on all national roads), and
    also by LA / Statutory Undertakers any road works sites carried out by Statutory Undertakers on the TERN network (in Ireland, on all national roads).

## Slide 23: Article 7 Data Management
EU Road Infrastructure Safety Management Directive – April 2012

## Slide 24: Annex II
EU Road Infrastructure Safety Management Directive – April 2012
The Annex’s
‘Shall Endeavour’-
it’s not mandatory,
just an obligation
to do your best!!!!

## Slide 25: Other issues – Implementation Dates
EU Road Infrastructure Safety Management Directive – April 2012
Implementation Dates
  Directive dated 18th Nov 2008
  Implement in Member States by 19th Dec 2010
  Guidelines to be adopted by 19th Dec 2011, and submitted by 19th March 2012
  Training Criteria adopted by 19th Dec 2011
    Transition until 19th Dec 2013, then all auditors on TERN must have ‘Cert of Competence’

## Slide 26
Harry Cullen
SPM Road Safety, National Roads Authority, Ireland
Chairman of CEDR Technical Group Road Safety
 hcullen@nra.ie
www.nra.ie
Thank you
Notes: Road Infrastructure Safety Management Directive
31/07/26
EU Road Infrastructure Safety Directive - Kilkenny October 2010
<number>